memo

equations of mass dynamics in finite volume
{dm} over {dt} = sum (m_flow) newline -. mass flow into volume is positive sign newline m=ρV newline {dm} over {dt} = {dρ} over {dt}*V newline ρ= {p} over {RT} newline {dρ} over {dt} = {1} over {R} {d} over {dt} ({p} over {T}) newline = = {1} over {R} { dot p T - p dot T } over { T^{2} } newline sum (m_flow) = {V} over {RT} dot p - {Vp} over {R T^{2}} dot T

equations of energy dynamics in finite-volume
{dU} over {dt} = sum (mh_flow) newline {dU} over {dt} = {d} over {dt}(mu) newline == {dm} over dt u - m {du} over {dt} newline u= h - pv newline == CpT- {p} over {ρ} newline == CpT- RT newline {du} over {dt}= {d} over {dt}(CpT-RT) newline == (Cp-T) {dT} over {dt} newline == (Cp-R) dot T newline {dU} over {dt} = {V} over {R T^2}( dot p T - p dot T )(Cp-R)T + m(Cp-R) dot T newline dotsvert newline == {V(Cp-R)} over {R} dot p + [-{Vp(Cp-R)} over {RT} + m(Cp-R)] dot T newline sum (mh_flow) = {V(Cp-R)} over {R} dot p + (Cp-R)[-{Vp} over {RT} + m] dot T

left [ matrix{{V} over {RT} # -{Vp} over {R T^{2}} ## {V(Cp-R)} over {R} # (Cp-R)[-{Vp} over {RT} + m]} right ] left [ binom {dot p}{dot T} right ] = left [ binom {sum (m_flow)}{sum (mh_flow)} right ] newline left [ binom {dot p}{dot T} right ] = left [ matrix{{V} over {RT} # -{Vp} over {R T^{2}} ## {V(Cp-R)} over {R} # (Cp-R)[-{Vp} over {RT} + m]} right ]^{-1} left [ binom {sum (m_flow)}{sum (mh_flow)} right ]

parameters / constants

: dotsaxis [1]

variables

: dotsaxis [1]

equations

: dotsaxis [1]

Memo:
計算式のmmlファイルへの保存：計算式ボックスを左クリックで選択　→　右クリック　→　「名前を付けてコピーを保存」　→　「MathML 2.0」を選択